## Slide 1: New Mexico 911 Program
Understanding NM911 GIS Data Assessment Reports
New Mexico APCO Statewide Conference
Santa Fe, Apr 5, 2024

## Slide 2: Earth Data Analysis Center, The University of New Mexico’s Role
Monthly Tasks
  GIS Data acquisition, processing, assessment, and reporting
  Technical support to Data Providers and PSAPs
  Create statewide NM911 Master Database
  Assisting data providers with corrections
Quarterly Tasks
  MSAG-ALI-GIS data comparison, and reporting
  Assisting data providers/PSAPs with corrections

## Slide 3: GIS Data Upload Status as of March 2024
NM911 GIS Data Status Dashboard https://nm911-hub.maps.arcgis.com

## Slide 4: GIS Data Model (Current/Legacy)
Adopted in September 2019
Required Layers
  Address Points
  Road Centerlines
  Addressing/Administrative Boundary*
  Emergency Service Zone (ESZ) Boundary
  Public Safety Answering Point (PSAP) Boundary
Optional Layers
  Public Facilities, Community Boundary, Hydrology, Railroads, Mile Markers, Bridges
* Provisioning boundary will be used if available. Required for Next Gen 9-1-1

## Slide 5: NG9-1-1 GIS Data Layers
Required | Strongly Recommended | Recommended
Road Centerlines | Other service boundary layers (ex: Coast guard, poison control, etc.) | Railroad centerline
Address Points | Street name alias table | Hydrology (streams & water bodies)
PSAP Boundary | Landmark name table | Cell sectors
Fire Boundary | Landmark name alias table | Location Markers
Police Boundary |  | 
EMS Boundary |  | 
Provisioning Boundary |  | 

## Slide 6
Collection | 
Conversion | 
Processing/ Assessment | 
Reporting | 
Aggregating & Publishing | 
Email notification to GIS POCs
Data Upload to the NM911 Data Portal
Notify GIS POCs & Receive Feedback
Create a version of NM911 geodatabase for each GIS data provider
Check for valid data attributes
Spatial and Tabular checks
Topology Checks
Data Reviewer Checks
Create Fishbone lines
Generate Monthly Data Assessment Reports, Quarterly MSAG/ALI/GIS Comparison Reports and corresponding error geodatabases
Upload reports and error geodatabases to the NM911 Data Portal
Aggregate address and road data to create a statewide master datasets
Check data formats
Update monthly error statistics for each data provider on the NM911 GIS Dashboard
Deliver to NM DFA for PSAP updates & publish to RGIS data clearinghouse for public access
If invalid
If invalid
Technical Assistance with Data upload, Understanding reports and error data & Data Correction
Crosswalk data to NM911 GIS Data Model
MSAG data download from Intrado (quarterly)
ALI data download from Intrado (once a year)
Parse data to GIS tables
Extract data per each PSAP boundary area
Extract and aggregate recent address and road data for all local jurisdictions within each PSAP boundary area
MSAG to GIS Data Comparison
ALI to GIS Data Comparison
Monthly GIS Data Validation Workflow
Quarterly GIS-MSAG-ALI Comparison Workflow
New Mexico 911 (NM911) Program GIS Data Workflow

## Slide 7: Data Collection
Data Providers were notified via e-mail each month
How: NM911 Data Portal https://portal.nm911.org/
When: 1st – 15th of each month
What: Address points, Road centerlines, and Boundaries
  Accepted data formats: Shapefiles (zipped or unzipped), File geodatabases (zipped)
Notes: If multiple uploads, duplicate data are resolved before data conversion process. Latest data are processed and all other previous uploads will be rejected.

## Slide 8: NM911 Data Portal
Acknowledgement if upload is a Success! No email – We try not to SPAM your inbox!!
As seen in the second half of each month.

## Slide 9: NM911 Data Portal

## Slide 10: NM911 Data Portal

## Slide 11: NM911 Data Portal

## Slide 12: Data Conversion
NM911 Data Portal Admin Tools
  NM911 Data Model
  Field Mapping/Crosswalk between local schema to state schema
  Data imported to State Schema
  Error feature classes are created if exists

## Slide 13: Data Assessment
QA/QC to ensure data integrity
Spatial & Tabular Accuracy Checks
Topology Checks
Data Reviewer Checks
Datasets: Road Centerlines, Address Points, Administrative/Addressing Boundary

## Slide 14: Data Assessment
 |  | DATA REVIEWER CHECKS
1 |  | Address Point Address Number Cannot Be 0, Negative, NULL Or Blank
2 |  | Address Point Address Number Should Be Within Road Centerline Address Range
3 |  | Address Point Full Road Name Must Match Road Centerline Full Road Name
4 |  | Address Point Has Invalid Geometry
5 |  | Address Point Must Not Have Duplicate Geometry
6 |  | Address Point Street Name Cannot Be Blank Or NULL
7 |  | NM911 Topology Checks
8 |  | Road Centerline Has Invalid Geometry
9 |  | Road Centerline Left High Address Must Be Odd
10 |  | Road Centerline Left Low Address Is Greater Than Left High Address
11 |  | Road Centerline Left Low Address Must Be Odd
12 |  | Road Centerline Length Must Not Be Less than 15 ft.
13 |  | Road Centerline Must Be Broken And Snapped At Road Intersections
14 |  | Road Centerline Must Not Have Dangles
15 |  | Road Centerline Must Not Have Duplicate Geometry
16 |  | Road Centerline Must Not Have Left Side Overlapping Address Range
17 |  | Road Centerline Must Not Have Right Side Overlapping Address Range
18 |  | Road Centerline Right High Address Must Be Even
19 |  | Road Centerline Right Low Address Is Greater Than Right High Address
20 |  | Road Centerline Right Low Address Must Be Even
21 |  | Road Centerline Should Not Be Multipart

## Slide 15: Data Analysis – Fishbone
Visually Compare road centerlines to address points
  Out of numerical order
  On the wrong side of the street
  On the wrong block
Only generated if the address point and road centerline data contains Community Name and ZipCodes

## Slide 16: Fishbone Analysis
GOOD

## Slide 17: Fishbone Analysis
BAD
Notes: Query data to identify data inaccuracies
Ex: Wrong side of the street or Block: show every fishbone that intersects a street centerline

## Slide 18: Fishbone Analysis
Notes: Red: Incorrect data. Longer lines indicate more serious error. i.e. valid address points are miles from where they should be

## Slide 19: Fishbone Analysis
Fix: Address range of the road centerline needs to be flipped odd/even

## Slide 20: Data Reporting

## Slide 21: Data Correction – Exceptions
Road Centerline Left Low & High Address Must Be Odd
Road Centerline Right Low & High Address Must Be Even
Road Centerline Left Low Address is Greater than Left High Address
Road Centerline Right Low Address is Greater than Right High Address
  Can be marked as Exceptions based on ground conditions
  Exception data column. Mark “Y” or “1” (based on the field data type: TEXT, INTEGER) if there is an exception and leave the column blank if no exception

## Slide 22: Data Correction – Topology
Roads Must Not Intersect or Touch Interior
  Road Centerline Must Be Broken and Snapped at the Intersection with an exception for overpass/underpass.
Address Point Must Be Properly Inside the Administrative Boundary
  Administrative Boundary can be replaced with Addressing Boundary of validation, if available.

## Slide 23: Data Correction – Address Points Examples
Address Point Address Number Cannot Be 0, Negative, Null or Blank
  Ex: 0 JUAN PEREA RD SE
Address Point Address Number Should Be Within Road Centerline Address Range
  Ex: 922 HILLSIDE DR SW

## Slide 24: Data Correction – Road Centerline Examples
Address Point Full Road Name Must Match Road Centerline Full Road Name
  Ex: VALLE VISTA RD NW
Road Centerline Must Not Have Right Side Overlapping Address Range
  Ex: SICHLER RD SW

## Slide 25: NM911 Master Database
Import data submitted by data providers after validation
Run geometry checks
Share data (road centerlines, address points)
  DFA for PSAP Map Updates
  Public on RGIS Geospatial Data Clearinghouse (shapefiles)
Road Centerlines,
Address Points - NM911 Master Database (Apr 2023)

## Slide 26: A Few Data Stats…
Chart: Record count
| Address Points | Road Centerlines
Dec 2018 | 943442 | 209255
Dec 2020 | 994426 | 211857
Dec 2022 | 1015750 | 212844
May 2023 | 1021682 | 213570

Chart: Improved Data Accuracy
| Dona Ana County (DA_CO) | Grant County (GR_CO) | Socorro County (SO_CO) | City of Hobbs (LEHOB) | Jicarilla Apache Nation (TRJIC) | City of Aztec (SJAZT) | Union County (UN_CO)
First Upload | 10496 | 6082 | 1336 | 1624 | 405 | 69 | 55
Latest Upload | 289 | 6265 | 1030 | 1283 | 2 | 7 | 5

## Slide 27: GIS-MSAG-ALI Comparison
Quarterly Assessments
Essential for Next Generation 911 (NG 9-1-1) data transition
NENA recommends a 98% match rate between the datasets
Data Providers and PSAPs must prioritize to improve data accuracy
Data for Comparison
  GIS – monthly data uploads from GIS Data Providers
  MSAG – quarterly data downloads from Intrado
  ALI – yearly data download from Lumen (formerly CenturyLink)

## Slide 28: GIS-MSAG-ALI Comparison
https://www.arcgis.com/apps/dashboards/ba1e3e23a1f24a299fec935a2751c6e2

## Slide 29: GIS-MSAG-ALI Comparison
Snapshot of Quarterly GIS-MSAG-ALI Comparison Stats, De Baca County – March 2022
MSAG and GIS Datasets used for Comparison
Notes: MSAG Record count – Source Data: 509 and GIS: 506 – eliminated Wireless or VOIP calls rows

## Slide 30: GIS-MSAG Comparison
Road Centerline data compared with MSAG records
Address columns, Community name, and ESN (Concatenated for left and right side of each segment to create unique identifier)
Results are generated in geodatabase and spreadsheet formats
Notes: Address range comparisons were performed on entire road segments and are reported as such. For example, consider a road segment CENTRALAVE|ALBUQUERQUE|00111. In the MSAG, this segment has a low of 100 and a high of 249. In the road centerline file, there are two segments, one with a low of 100 and a high of 149, and another with a low of 200 and a high of 299. In this case, the MSAG segment will report that it does not have the range 250-299. In the road centerline, both segments will report that they are missing the range 150-199.

## Slide 31: GIS-MSAG Comparison – Interpreting Results
REPORT | COMPARISON
Exact MSAG match | 13THMILERD¦FORTSUMNER¦00940
Does not have an MSAG match | ANTELOPERD¦ROSWELL¦00940
Does not have a road centerline match | LYNXRD¦FORTSUMNER¦00940
Not in NM911 road- Rng: 3466-3968 | BILLYTHEKIDDR¦FORTSUMNER¦00942
Not in NM911 road- Val: 3097 | CLAYFLATRD¦FORTSUMNER¦00940
Not in MSAG- Rng: 800-1299, Val: 1499 | EDUNNHL¦FORTSUMNER¦00943
Not in MSAG- Val: 1300 | EFOLEYAVE¦FORTSUMNER¦00943

## Slide 32: GIS-MSAG Comparison – Interpreting Results
BILLYTHEKIDDR|FORTSUMNER|00942 – Not in NM911 road- Rng: 3466-3968
Derived from GIS data (road centerlines)
Derived from MSAG from 911NET
In MSAG data, address range 3466 – 3969 is duplicated for ESN 942 & 943
In GIS data, address range 3466-3968 is part of ESN 943.
Fix: Data Providers & PSAPs must coordinate to establish the authoritative dataset and update the non-authoritative dataset!

## Slide 33: GIS-MSAG Comparison – Interpreting Results
CLAYFLATRD|FORTSUMNER|00940 – Not in NM911 road- Val: 3097
In GIS data, Value 3097 is part of YESO and not in FORT SUMNER. This is a valid error & No Correction Needed!

## Slide 34: GIS-MSAG Comparison – Interpreting Results
EDUNNHL|FORTSUMNER|00943 – Not in MSAG- Rng: 800-1299, Val: 1499
  EDUNNHL|FORTSUMNER|00940 - Does not have a road centerline match
Derived from GIS data (road centerlines)
Derived from MSAG from 911NET
Fix: Data Providers & PSAPs must coordinate to establish the authoritative dataset and update the non-authoritative dataset!

## Slide 35: GIS-MSAG Comparison – Interpreting Results
EFOLEYAVE|FORTSUMNER|00943 – Not in MSAG- Val: 1300
  EFOLEYAVE|FORTSUMNER|00940 – Does not have a road centerline match
Derived from GIS data (road centerlines)
Derived from MSAG from 911NET
Fix: Data Providers & PSAPs must coordinate to establish the authoritative dataset and update the non-authoritative dataset!

## Slide 36: GIS-ALI Comparison
Tabular ALI data are compared with GIS address point data
If no exact matches found in the addresses then those records will be compared with Road Centerline data to see if the address fits within the address range of the corresponding segment
Address Number, Road Name columns (STR_DIR, STR_PRETYPE, STR_NAME, STR_SUFFIX, POST_DIR), MSAG Community, and ESN

## Slide 37: GIS-ALI Comparison – Interpreting Results
Exact NM911 Address Point Match
Address Points Where Clause
  ADD_NUMBER=1115 AND MSAG_COM='FORT SUMNER' AND (ADD_SUFFIX IS NULL or ADD_SUFFIX='') AND (STR_DIR IS NULL or STR_DIR='N') AND STR_NAME_1 = '10TH HL' and ( ESN = '943' OR ESN= '00943')
PHONE_NUMBER | ADD_NUMBER | ADD_SUFFIX | STR_DIR | STR_NAME_1 | COMMUNITY | ESN | DPID
5753552218 | 1115 |  | N | 10TH HL | FORT SUMNER | 00943 | DB_CO

## Slide 38: GIS-ALI Comparison – Interpreting Results
No Match found in NM911 Address Points
Address Point Where Clause:
  ADD_NUMBER=709 AND MSAG_COM='FORT SUMNER' AND (ADD_SUFFIX IS NULL or ADD_SUFFIX='') AND (STR_DIR IS NULL or STR_DIR='N') AND STR_NAME_1 = '2ND ST' and ( ESN = '943' OR ESN= '00943')
Road Centerline Where Clause:
  COMPARE ='N2NDST|FORTSUMNER|00943' AND CAST(HIGH AS INTEGER) >= 709 AND CAST(LOW AS INTEGER) <=709
PHONE_NUMBER | ADD_NUMBER | ADD_SUFFIX | STR_DIR | STR_NAME_1 | COMMUNITY | ESN | DPID
5753557131 | 709 |  | N | 2ND ST | FORT SUMNER | 00943 | DB_CO

## Slide 39: GIS-ALI Comparison – Interpreting Results
No Match found in NM911 Address Points or Road Centerlines
Address Point Where Clause:
  ADD_NUMBER=339 AND MSAG_COM='FORT SUMNER' AND (ADD_SUFFIX IS NULL or ADD_SUFFIX='') AND (STR_DIR IS NULL or STR_DIR='S') AND STR_NAME_1 = '14TH ST' and ( ESN = '941' OR ESN= '00941')
Road Centerline Where Clause:
  COMPARE ='S14THST|FORTSUMNER|00941' AND CAST(HIGH AS INTEGER) >= 339 AND CAST(LOW AS INTEGER) <=339
PHONE_NUMBER | ADD_NUMBER | ADD_SUFFIX | STR_DIR | STR_NAME_1 | COMMUNITY | ESN | DPID
5753556204 | 339 |  | S | 14TH ST | FORT SUMNER | 00941 | DB_CO

## Slide 40: NM911 Website
URL https://www.nm911.org/
Program related information
  GIS data standards
  Funding eligible items for PSAPs and GeoData Providers
  Eligible training options – GIS
  Links to download GIS datasets
  FAQs
  Presentations
  Training Videos
  Etc…

## Slide 41: NM911 ArcGIS Hub
https://nm911-hub.maps.arcgis.com/home/index.html

## Slide 42: NMDPS CAD GIS Support
EDAC is under contract with Department of Public Safety (NMDPS) for GIS Support of their Computer Aided Dispatch (CAD) System
This contract is not related to the New Mexico 911 Program GIS Support
Routable Road Network Data – Available of Request
For questions regarding their data, workflow, or other inquires, please contact:
    Brian Keller
    GIS Manager, EDAC
    Email: bkeller@edac.unm.edu
    Phone: (505) 277-3622 x228

## Slide 43: Contact Us
Technical Questions
  Sandeep Talasila
  Earth Data Analysis Center, UNM
  Email: nm911@edac.unm.edu
  Phone: (505) 277-3622 x250
  NM911 Data Portal: Submit a support request
General Questions
  Tyler Fossett
  NM911 GIS Coordinator
  NM Department of Finance & Administration
  Email: Tyler.Fossett@dfa.nm.gov
  Phone: (505) 500-5587